## Slide 1: Purpose of the course
An introduction to the organization and design of computers – principles, techniques, issues…
Prerequisites:
  Assembly programming (the view of computer (processor) at the register’s level)
  Basic knowledge of Boolean algebra and logic circuits – AND/OR gates, and Boolean functions performed by them
§2.1 Introduction

## Slide 2: Purpose of the course
It is a common practice to discuss the principles of computer HW/SW design based on a specific, existing computer structure
The underlying computer this course is based on is called MIPS
  Microprocessor without Interlocked Pipelined Stages
  Millions of Instructions Per Second
§2.1 Introduction

## Slide 3: Purpose of the course
The instruction set of a computer describes how the computer functions at the lowest (register/memory) level
We start by examining the instruction set of MIPS
Idea – We want to design a processor. The first thing to do is to specify the computer’s operations, i.e. what this computer can do
§2.1 Introduction

## Slide 4: Chapter 2
Instructions: Language of the Computer

## Slide 5: Instruction Set
It is the repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simple instructions simple implementation
However, many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 6: Instruction Set
Two computer design paradigms
– CISC vs. RISC
  CISC: Complex Instruction Set Computer
    Powerful, complex instructions, shorter programs, but need more complex hardware
  RISC: Reduced Instruction Set Computer
    Smaller, simple instruction set, need more instructions for complex operations
  MIPS belongs to the RISC category
§2.1 Introduction

## Slide 7: The MIPS Instruction Set
Used as the example throughout this course
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Typical of many modern ISAs (Industry Standard Architecture)

## Slide 9: Arithmetic Operations
add/subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
where a,b,c are all registers in the processor
All arithmetic operations have the same form (sub a, b, c; mul a, b, c …)
  Favors regularity
§2.2 Operations of the Computer Hardware

## Slide 10: Arithmetic Operations
Design Principle 1: Simplicity favors regularity
  Regularity/uniformity makes hardware implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 11: Arithmetic Example
Most programmers write programs in high-level languages, such as Java or C
Example C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 12: Register Operands
In computers, arithmetic instructions use registers to hold operands
MIPS has a 32 × 32-bit register set
  Used for holding data that are currently processed
  Registers are numbered from 0 to 31
  32-bit data called a “word”
We can assign names to registers
  $t0, $t1, …, $t9 for temporary values (10 registers)
  $s0, $s1, …, $s7 for saved variables (8 registers)
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware
Notes: So, the total size of the register file =
32 \text{ registers} \times 32 \text{ bits} = 1024 \text{ bits (128 bytes)}

## Slide 13: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, g, h, i, j $s0, $s1, $s2, $s3, $s4
  variables registers
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 14: Memory Operands
Main memory used for composite and large amount of data
  Arrays, structures (Java objects), dynamic data
Registers
in here

## Slide 15: Memory Operands
To apply arithmetic operations, need to
  Load values from memory into registers (g,h,i,j)
  Store result from register to memory (f)
Memory is byte-addressed
  Each address holds an 8-bit byte
Words are aligned in memory
  Each word occupies 4 consecutive addresses
  So a word address must be a multiple of 4

## Slide 16: Memory Operands
MIPS uses “Big Endian” convention
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 17: Registers vs. Memory
Registers are much faster to access and operate on than memory
Operating on memory data requires
load-word (lw) and store-word (sw)

## Slide 18: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index [8] requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register
in memory

## Slide 19: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index [8] requires offset of 32
  Index [12] requires offset of 48
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
in memory

## Slide 20: Registers vs. Memory
Compiler should use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!
    Out of the range of this course

## Slide 21: Immediate Operands
Constant data specified in an instruction
  add immediate
addi $s3, $s3, 4 # 4 is part of instruction
No “subtract immediate” instruction
  Just use a negative constant
  addi $s2, $s1, -1 # minus 1
  addi $s2, $s1, -7 # minus 7
Design Principle 3: Make the common case fast
  Small constants are common in programming
  Immediate operand avoids a load instruction

## Slide 22: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Fixed value, always contains 0
  Cannot be overwritten
Useful for some commonplace operations
  E.g., move between registers
  add $t2, $s1, $zero
  Equivalent to
  move $t2, $s1

## Slide 24: Unsigned Binary Integers
Given an n-bit binary number
  bn-1bn-2… b1b0
Its decimal value x
  x = bn-1×2n-1 + bn-2×2n-2 +… + b1×21 + b0×20
Range: 0 to +2n – 1
Example:
  n = 4; Range: 0 to 15 (0000 – 1111)
  n = 5; Range: 0 to 31 (00000 – 11111)
§2.4 Signed and Unsigned Numbers

## Slide 25: Unsigned Binary Integers
§2.4 Signed and Unsigned Numbers
MIPS Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0×231 + 0×230 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + 0 + … + 8 + 0 +2 +1 = 1110
Using 32 bits
  0 to +4,294,967,295
  (00…0000 to 11…1111)

## Slide 26: 2s-Complement Signed Integers
Given an n-bit binary number
  bn-1bn-2… b1b0
Its decimal value
  x = −bn-1×2n-1 + bn-2×2n-2 +… + b1×21 + b0×20
Range: −2n-1 to +2n-1 − 1
Example:
  n = 4; Range: -8 to +7 (1000 – 0111)
  n = 5; Range: -16 to +15 (10000 – 01111)

## Slide 27: 2s-Complement Signed Integers
MIPS Example
  1111 1111 1111 1111 1111 1111 1111 11002 = −1×231 + 1×230 + … + 1×22 +0×21 + 0×20 = −2,147,483,648 + 2,147,483,644 = −410
Using 32 bits
  −2,147,483,648 to +2,147,483,647
  (100…000 to 0111…111)

## Slide 28: 2s-Complement Signed Integers
Bit 31 is used as sign-bit
  1: the number is negative
  0: the number is non-negative (positive or zero)
+2n – 1 can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some special numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000 (−2n – 1)
  Most-positive: 0111 1111 … 1111 (+2n – 1 − 1)

## Slide 29: Signed Negation
Step 1: Complement all bits
Step 2: Add 1
  Complement means 1 → 0, 0 → 1 (flip)
Example: negate +2
  +2 = 0000 0000 … 00102
  −2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 30: Sign Extension
Representing a number using more bits
  Have to preserve the original numeric value
In MIPS instruction set
  addi: need to extend immediate value
  lb, lh: load-byte (8-bits), load-half (16-bits)
  need to extend loaded byte/halfword
  beq, bne: need to extend the (jump) displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 32: Representing Instructions
Instructions are also encoded in binary bits
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Try to encode operation code (opcode), register numbers, constants… in just a few formats
Register numbers (IDs):
  From register #0 to register #31
  $t0 – $t7 are registers 8 – 15
  $t8 – $t9 are registers 24 – 25
  $s0 – $s7 are registers 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 33: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (not used, 00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 34: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
0 2 3 2 4 0 2 0 16

## Slide 35: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | C | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | D | 1101
2 | 0010 | 6 | 0110 | A | 1010 | E | 1110
3 | 0011 | 7 | 0111 | B | 1011 | F | 1111
Example: ECA8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 36: MIPS I-format Instructions
Immediate arithmetic – addi
load/store – lw/sw
  rt: destination or source register number
  Constant: –215 to +215 – 1 (-32,768 to +32767)
  Address: offset added to base address in rs
Example: addi $t0, $s1, 4
Example: lw $t1, 100($s1)
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 37: Stored Program Computers
Instructions are represented in binary bits, just like data
Instructions and data both stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different (but compatible) computers
The BIG Picture

## Slide 38: Shift Operations
Examples:
  Sll t2, s0, 8
  srl t3, s1, 4
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 39: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left, and fill with 0 bits (on right)
  sll by i bits = multiplies by 2i
Shift right logical
  Shift right, and fill with 0 bits (on left)
  srl by i bits = divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 40: AND Operations
Useful to mask bits in a word
  0 & x = 0; 1 & x = x
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0
(select the 4 shaded bits in $t2)
(selector register)

## Slide 41: OR Operations
Useful to include bits in a word
  0 | x = x; 1 | x = 1
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0
(setter register)

## Slide 42: NOT Operations
Useful to invert (flip) bits in a word
  Change 0 → 1, and 1 → 0
MIPS has 3-operand NOR instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
($t0 ← NOT($t1))
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 44: Stored Program Computers
Instructions are represented in binary bits, just like data
Instructions and data both stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different (but compatible) computers
The BIG Picture

## Slide 45: Instruction Formats
R-format: Arithmetic, logical, shift
I-format: immediate, load/store
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 46: Conditional Operations
Branch to a labeled instruction if some condition is true; otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 47: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else # i=s3, j=s4
add $s0, $s1, $s2 # f = g+h
j Exit
Else: sub $s0, $s1, $s2 # f = g-h
Exit: …
Assembler calculates addresses

## Slide 48: Compiling Loop Statements
C code:
while (save[i] == k) i++;
  Counting the number of “k” in array save[]
  i = $s3, k = $s5, address of save = $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 # t1 ← i*4 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 # i += 1 j Loop Exit: …

## Slide 49: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 50: More Conditional Operations
Set a register to 1 if a condition is true; otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, const
  if (rs < const) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 51: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  <, ≥ combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized (since clock is used by all instructions)
beq and bne are the common case
  =, ≠ combining with branch happen to result in a quicker hardware
A good example of design compromise

## Slide 52: Signed vs. Unsigned
slt, slti are signed comparison
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 54: Procedure (Method) Calling
proc(x, y, z);
……
Steps happening:
  Place parameters (x, y, z) in registers
  Transfer control to procedure (or method)
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware

## Slide 55: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29) – top of stack
$fp: frame pointer (reg 30) – bottom of stack
$ra: return address (reg 31)

## Slide 56: Procedure Call Instructions
Procedure call: jal (“jump and link”)
jal L # L – Procedure Label
  Address of the next instruction put in $ra
  (automatic, by hardware)
  Jumps to target address
Procedure return: jr (“jump register”)
jr $ra # register 31
  Copies $ra to program counter PC

## Slide 57: Some Special Registers
Every time a method is called (executed), a “stack” is built for this call
The stack is eliminated after the call ends
$sp: stack pointer (reg 29) – top of stack
$fp: frame pointer (reg 30) – bottom of stack
$ra: return address (reg 31)

## Slide 58: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, h, i, j in $a0, $a1, $a2, $a3 (reg’s 4 – 7)
  Use $s0 for f (hence, need to save current content of $s0 on stack, and then restore)
  Result in $v0 (register 2)

## Slide 59: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
$s0 will be used for f
Procedure body
Restore $s0
Result
Return

## Slide 60: Non-Leaf Procedures
Procedures that call other procedures
For the nested call, caller needs to save the following into stack:
  Its return address (stack ← $ra)
  Any arguments and temporaries needed after the call
Restore from the stack after the nested call

## Slide 62: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 63: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in $a0: $a0 = n
  Result in $v0: $v0 = n×(n-1) ×…×2×1

## Slide 64: Local Data on the Stack
High address
Low address
$fp
←
←
←
←
←
←
$fp
$sp
(reg 29)
$sp
$sp
Before a call
During a call
After a call
Return address
to caller
Arguments and
other stuff
$fp
(reg 30)

## Slide 65: Non-Leaf Procedure Example
MIPS code: Go over a small example to see its working
fact: # addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
2000:
2040:

## Slide 66: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 67: Non-Number Data
Byte-encoded character sets
  ASCII: 128 characters (7 bits)
    95 graphic, 33 control
  Latin-1: 256 characters (8 bits)
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People

## Slide 68: Byte/Halfword Operations
MIPS can load and store byte/halfword
  byte: 8-bit; halfword: 16-bit
  Sign-extend to 32 bits in rt:
lb rt, offset(rs); lh rt, offset(rs)
  Zero-extend to 32 bits in rt:
lbu rt, offset(rs); lhu rt, offset(rs)
  Store just rightmost byte/halfword:
sb rt, offset(rs); sh rt, offset(rs)

## Slide 69: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i++; }
  Addresses of x, y in $a0, $a1
  i in $s0

## Slide 70: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 72: 32-bit Constants
0000 0000 0011 1101 0000 0000 0000 0000
Most constants are small (a fact of life)
  16-bit immediate is sufficient
For the (occasional) large 32-bit constant
lui rt, const # load upper-half
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lui $s0, 61
0000 0000 0011 1101 0000 1001 0000 0000
ori $s0, $s0, 2304
§2.10 MIPS Addressing for 32-Bit Immediates and Addresses
61
2304

## Slide 73: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
  (Ex. beq $2, $3, L1)
Most branch targets are to a near target
  Forward or backward
op
rs
rt
address (offset)
6 bits
5 bits
5 bits
16 bits

## Slide 74: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
  (Ex. beq $2, $3, L1)
Most branch targets are to a near target
  Forward or backward
op
rs
rt
address (offset)
6 bits
5 bits
5 bits
16 bits
?

## Slide 75: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
  (Ex. beq $2, $3, L1)
Most branch targets are to a near target
  Forward or backward
op
rs
rt
address (offset)
6 bits
5 bits
5 bits
16 bits
MIPS uses PC-relative addressing
  Target address = PC + (offset × 4)
  PC already incremented by 4 by this time

## Slide 76: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
  (Ex. j L2)
op
word-address
6 bits
26 bits
(Pseudo) Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 77: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 2 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 78: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler recompile the code
Example
  beq $s0,$s1, L1 #if L1 > 16-bits
  ↓
  bne $s0,$s1, L2 #L2 nearby addr j L1 #j instruction L2: … #holds larger addr

## Slide 79: Summary: Addressing Mode
addi rs, rt, immed
add rd, rs, rt
lw rs, offset(rt)
beq rs, rt, L1
j L2

## Slide 81: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization

## Slide 82: Synchronization in MIPS
Load linked: ll rt, offset(rs)
Store conditional: sc rt, offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4

## Slide 83: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 84: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assemblfigmentser temporary

## Slide 85: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 86: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 87: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 88: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 89: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code

## Slide 90: Starting Java Applications
Simple portable instruction set for the JVM
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine

## Slide 91: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  /* swap contents of v[k],v[k+1] */ void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in $a0, k in $a1, temp in $t0
§2.13 A C Sort Example to Put It All Together

## Slide 92: The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k] in $t1)
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine
Note: the stack is not used, because the procedure doesn’t use any registers whose content need to be reserved

## Slide 93: The Sort Procedure in C
Non-leaf (calls swap)
void sort (int v[], int n)
{
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j=i–1; j>=0 && v[j]>v[j+1]; j-=1){
  swap(v,j); /*calls swap*/
  }
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1
  Insertion Sort
  Start comparing from left

## Slide 94: The Sort Procedure in C
Non-leaf (calls swap)
void sort (int v[], int n)
{
  int i, j;
  for (i = 0; i < n; i += 1){
  for (j = n–2; j >= i; j -= 1)
  if (v[j]>v[j+1])
  swap(v,j); /*calls swap*/
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1
  Bubble Sort
  Start comparing from right

## Slide 95: The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 96: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 97: Concluding Remarks
Principles for design of instruction set
  1. Simplicity ⇒ regularity
  2. Smaller ⇒ faster
  3. Make the common case fast
  4. Good design demands good compromises
§2.19 Concluding Remarks

## Slide 98: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%