## Slide 1: Chapter 3
Arithmetic for Computers

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result goes out of range
  Adding +ve and –ve operands ⇒ no overflow
  Adding two +ve operands (both sign bits = 0)
    Overflow if result sign is 1 (negative result)
  Adding two –ve operands (both sign bits = 1)
    Overflow if result sign is 0 (positive result)

## Slide 4: Integer Subtraction
Always do “add”
For subtraction, add negation of the 2nd operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand ( ex. –5 – (+6) )
    Overflow if result sign is 0 (positive result)
  Subtracting –ve from +ve operand ( ex. 5 – (–6) )
    Overflow if result sign is 1 (negative result)

## Slide 5: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action

## Slide 6: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
multiplicand
1000
1001

## Slide 7: Multiplication
Start with long-multiplication approach
1000
× 1111
1000
1000
1000
1000
1111000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
multiplicand
1000
1111

## Slide 8: Multiplication
Start with long-multiplication approach
1000
× 1111
1000
10000
100000
1000000
1111000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
multiplicand
1000
1111

## Slide 9: Multiplication Hardware
Initially 00000000
1000
1111
multiplicand

## Slide 10: Multiplication
Start with long-multiplication approach
1000
× 1111
1000
10000
100000
1000000
1111000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
multiplicand
1000
1111
Fixed

## Slide 11: Multiplication
§3.3 Multiplication
Fixed
+
A
B
+
A
B
Fixed
0
0
0
0
A
B
A
B

## Slide 12: Multiplication
Start with long-multiplication approach
1000
× 1111
1000
10000
100000
1000000
1111000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
multiplicand
1000
1111
Fixed
32 bits

## Slide 13: Optimized Mult Hardware
Perform steps in parallel: add/shift
Multiplicand register: 32 bits
ALU: 32 bits
Multiplier register: Eliminated
One cycle per partial-product addition
Multiplier
1000
1111
0000

## Slide 15: Faster (Parallel) Multiplier
To speed up mult op, use more adders
  Cost/performance tradeoff
Can be pipelined
  Multiple multiplications performed in parallel
16 adders
8 adders
1 adder

## Slide 16: How does MIPS Multiply
Two 32-bit dedicated registers holding product
  HI: most-significant 32 bits
  LO: least-significant 32-bits (HI/LO not directly accessible by programmers)
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO;
    Very expensive operation! (32 rounds of add)
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt (“small” mult)
    Least-significant 32 bits of product → rd

## Slide 17: Division
Check for 0 divisor (can’t do)
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Always do the subtract; if remainder goes < 0, then add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
2n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 18: Division
Check for 0 divisor (can’t do)
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Always do the subtract; if remainder goes < 0, then add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
0010
0101
1010
-1000
10
2n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 19: Division
Check for 0 divisor (can’t do)
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Always do the subtract; if remainder goes < 0, then add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
10
1000 0001010
-1000
2n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 20: Division
Check for 0 divisor (can’t do)
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Always do the subtract; if remainder goes < 0, then add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
100
1000 0001010
-1000
2n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 21: Division
Check for 0 divisor (can’t do)
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Always do the subtract; if remainder goes < 0, then add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 0001010
-1000
2n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 22: Division Hardware
Initially divisor in left half
divisor
Initially dividend

## Slide 23: Optimized Divider
At the end: Remainder Quotient
Shift right: multiplication
Shift left: division
1001010
1000
One cycle per partial-remainder subtraction

## Slide 24: Optimized Divider
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 25: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 27: Floating Point
Representation for non-integer numbers
  Including very small and very large numbers
float and double in C/C++, Java
Like scientific notation
  +0.002 × 10–4
  +987.02 × 109
  –2.34 × 1056
In binary
  ±1.xxxxxxx2 × 2yyyy
normalized: one non-zero digit before decimal
not normalized
§3.5 Floating Point

## Slide 28: Floating Point Standard
Universal floating point standard:
Two representations
  Single precision (32-bit), for float
  Double precision (64-bit), for double

## Slide 29: Single Precision
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
S
Exponent
Fraction
single: 8 bits (signed)
single: 23 bits
S
yyyyyyyy
xxxxxxxxxxxxxxxxxxxxxx
single: 8 bits (signed)
single: 23 bits

## Slide 30
S
Exponent
Fraction
S
yyyyyyyy
xxxxxxxxxxxxxxxxxxxxxx
Single/double: 8/11 bits (signed)
Single/double: 23/52 bits
To make exponent unsigned
    Single: Bias = 127
    Double: Bias = 1023
Floating-Point Numbers
Single/double: 8/11 bits (signed)
Single/double: 23/52 bits

## Slide 31: Biased exponents
In processing floating numbers, we need to compare exponents quickly
But in 2’s complement, a negative number “looks like” bigger than positive one
In hardware, it is quicker to compare two unsigned numbers than signed ones
Hence the idea of bias: turn all exponents into positive (i.e. unsigned) for comparison purpose

## Slide 32: Biased exponents
Example: 4-bit signed numbers
Let bias = 7
-7 + 7 = 0000 biased exponent
-6 + 7 = 0001
-5 + 7 = 0010
-4 + 7 = 0011
-3 + 7 = 0100
-2 + 7 = 0101
-1 + 7 = 0110
-0 + 7 = 0111
1 + 7 = 1000
2 + 7 = 1001
3 + 7 = 1010
4 + 7 = 1011
5 + 7 = 1100
6 + 7 = 1101
7 + 7 = 1110
8 + 7 = 1111
real exponent

## Slide 34
S
Exponent
Fraction
S
yyyyyyyy
xxxxxxxxxxxxxxxxxxxxxx
Single/double: 8/11 bits (signed)
Single/double: 23/52 bits
To make exponent unsigned
    Single: Bias = 127
    Double: Bias = 1023
Floating-Point Numbers
Single/double: 8/11 bits (signed)
Single/double: 23/52 bits

## Slide 35: Biased exponents
In exponent field: actual exponent + Bias
To make exponent unsigned
    Single precision: Bias = 127
    Double precision: Bias = 1023

## Slide 36: Floating-Point Example
Represent –0.7510
  –0.7510 = –0.112 = –1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 37: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00 ?
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
– (1.012) × 2(129 – 127)
  = – 1.25 × 22
  = – 5.0

## Slide 38: Single-Precision Range
Exponents 00000000 and 11111111 reserved for special purposes, not for “ordinary” values
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Smallest fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  Exponent: 11111110 (= 25410)  actual exponent = 254 – 127 = +127
  Largest fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 39: Double-Precision Range
0000…00 and 1111…11 not used for exponents
  Reserved for special purposes
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Smallest fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110 (= 204610)  actual exponent = 2046 – 1023 = +1023
  Largest fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 40: Floating-Point Precision
Relative precision
  interval between numbers
  smallest interval between numbers
  Single: approximately 2–23
    2–23 = 10–?
    Equivalent to 23 × log102 ≈ 23 × 0.3
    ≈ 6 decimal digits of precision
  Double: approximately 2–52
    2–52 = 10–?
    Equivalent to 52 × log102 ≈ 52 × 0.3
    ≈ 16 decimal digits of precision

## Slide 41: Floating-Point Range/Precision
S
Exponent
Fraction
single: 8 bits (signed)
single: 23 bits
S
Exponent
Fraction
double: 11 bits (signed)
double: 52 bits
Range: ±1.2 × 10–38 – 3.4 × 10+38
Precision: 0.000001
Range: ±2.2 × 10–308 – 1.8 × 10+308
Precision: 0.0000000000000001
To put in perspective, according to estimates, the whole Milky Way Galaxy contains approximately 1067 atoms

## Slide 42: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers (smaller than the smallest number that can be represented in this computer)
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 43: Infinities and NaN
Exponent = 111...1, Fraction = 000...0
  ±Infinity (0111111110000…00)
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., x / 0.0
  Can be used in subsequent calculations

## Slide 45: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.612 × 10–1
1. Align decimal points
  Right-shift number with smaller exponent (why?)
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102
Right-shifted

## Slide 46: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Right-shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.062510
Right-shifted

## Slide 47: FP Adder Hardware
Much more complex than an integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
So FP adder usually takes multiple cycles

## Slide 48: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4
Integer adder

## Slide 49: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 50: Floating-Point Multiplication
4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.2187510

## Slide 51: FP Instructions in MIPS
FP (Floating-Point) hardware is coprocessor 1
  Adjunct processor that extends the ISA (Industry Standard Architecture)
Separate FP registers
  32 single-precision:
  $f0, $f1, … $f31
  Paired for double-precision (16 pairs):
  [$f0/$f1], [$f2/$f3], … [$f30/$f31]
  Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s

## Slide 52: FP Instructions in MIPS
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1 # c1 = coprocessor1
    e.g., ldc1 $f8, 32($sp)

## Slide 53: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx = eq, lt, le, …)
  Sets or clears FP condition-code bit
    e.g., c.lt.s $f3, $f4 # a condition code is set
Branch on FP condition code true or false
  bc1t, bc1f # t/f set by previous inst.
    e.g., bc1t TargetLabel # goto TargetLabel if true

## Slide 54: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals (5.0, 9.0, 32.0) in global memory space (pointed by register $gp)
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) # using c1 lwc1 $f18, const9($gp) div.s $f16, $f16, $f18 # f16=5.0/9.0 lwc1 $f18, const32($gp) sub.s $f18, $f12, $f18 # fahr-32.0 mul.s $f0, $f16, $f18 jr $ra

## Slide 55: FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k;
for (i = 0; i! = 32; i = i + 1) for (j = 0; j! = 32; j = j + 1) for (k = 0; k! = 32; k = k + 1) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2

## Slide 56: FP Example: Array Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …

## Slide 57: FP Example: Array Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1

## Slide 58: Interpretation of Data
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and finite precision
  Need to account for this in programs
The BIG Picture

## Slide 59: Note on Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i ?
  Only works for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2 (not –1)
  c.f.
    111110112 >> 2 = 001111102 = +62
§3.8 Fallacies and Pitfalls

## Slide 60: Note on Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
§3.6 Parallelism and Computer Arithmetic: Associativity
Need to validate parallel programs under varying degrees of parallelism

## Slide 61: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to real numbers
Bounded range and precision
  Operations can overflow and underflow
MIPS ISA
  Core instructions: 54 most frequently used
    100% of SPECINT, 97% of SPECFP (almost all MIPS instructions are used in benchmarks)
  Other instructions: Less frequent
  Meaning: MIPS is characteristic and typical
§3.9 Concluding Remarks