## Slide 1
Appendix D Mapping Control to Hardware
Copyright © 2014 Elsevier Inc. All rights reserved.

## Slide 2
The longest cycle is divided into 5 smaller cycles
  IF: Instruction Fetch from memory (IF)
  ID: Instruction Decode & register read (ID)
  EX: EXecute operation or calculate address (EX)
  MEM: Access MEMory operand (MEM)
  WB: Write result Back to register (WB)
R-Type: add $a, $b, $c – 1-2-3-5
Load: lw $a, offset ($b) – 1-2-3-4-5
Store: st $a, offset ($b) – 1-2-3-4
Branch: beq $a, $b, L1 – 1-2-3
common

## Slide 3: Multiclock Cycle Design
All control signals generated at the same time
Control signals generated at different times in different cycles

## Slide 4: Multiclock Cycle Datapath

## Slide 5
cf. Singleclock Cycle Datapath

## Slide 6: Finite State Machines
A finite state machine (FSM) is a computation model that can be implemented with hardware/software, and can be used to represent sequential logics

## Slide 7: Finite State Machines
A finite state machine (FSM) is a computation model that can be implemented with hardware/software, and can be used to represent sequential logics
It can be used as a tool to design/implement the multiclock control unit

## Slide 8: Finite State Machines
A finite state machine (FSM) is a computation model that can be implemented with hardware/software, and can be used to represent sequential logics
Here a “state” is a set of control signals at a certain stage (cycle) of an instruction

## Slide 9
9
Copyright © 2014 Elsevier Inc. All rights reserved.
The finite-state diagram for multicycle control
Each circle is the diagram is a “state”
Beginning of instruction
End of instruction

## Slide 10: Finite State Machines
Q: How to represent a “state”?
A: Use a register
Since there are 10 different states, we need a 4-bit register
The 10 states are numbered as 0-9:
state0=0000, state1=0001, state2=0010, state3=0011, state4=0100,
state5=0101, state6=0110, state7=0111, state8=1000, state9=1001

## Slide 11: Multiclock Cycle Datapath

## Slide 12
12
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.2 The control unit for MIPS will consist of some control logic and a register to hold the state. The state register is written at the active clock edge and is stable during the clock cycle
?

## Slide 13
13
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.3 The logic equations for the control unit shown in a shorthand form. Remember that “1” stands for OR in logic equations. The state inputs and NextState outputs must be expanded by using the state encoding. Any blank entry is a don’t care.
16 Control signals
Next states
+

## Slide 14
PCWrite = State0 + State9
PCWriteCond = State8
IorD = State3 + State5
MemRead = ……
……
= +
=
= +
……
……

## Slide 15
15
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.4 The truth tables are shown for the 16 datapath control signals that depend only on the current-state input bits, which are shown for each table. Each truth table row corresponds to 64 entries: one for each possible value of the six Op bits. Notice that some of the outputs are active under nearly the same circumstances. For example, in the case of PCWriteCond, PCSource0, and ALUOp0, these signals are active only in state 8 (see b, i, and k). These three signals could be replaced by one signal. There are other opportunities for reducing the logic needed to implement the control function by taking advantage of further similarities in the truth tables.

## Slide 16
16
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.1 The finite-state diagram for multicycle control.

## Slide 17
 | NS3 | NS2 | NS1 | NS0
NextState0 | 0 | 0 | 0 | 0
NextState1 | 0 | 0 | 0 | 1
NextState2 | 0 | 0 | 1 | 0
NextState3 | 0 | 0 | 1 | 1
NextState4 | 0 | 1 | 0 | 0
NextState5 | 0 | 1 | 0 | 1
NextState6 | 0 | 1 | 1 | 0
NextState7 | 0 | 1 | 1 | 1
NextState8 | 1 | 0 | 0 | 0
NextState9 | 1 | 0 | 0 | 1
NS2
NS3
NS0
NS1
NS0 = NextState1 + NextState3 + NextState5 + NextState7 + NextState9
NS1 = NextStat2 + NextStat3 + NextStat6 + NextStat7
NS2 = ……
NS3 = ……

## Slide 18
NS0 = NextState1 + NextState3 + NextState5 + NextState7 + NextState9
NextState1 = State0
NestState3 = State2  (Op=‘lw’)
NestState5 = State2  (Op=‘sw’)
NestState7 = State6
NestState9 = State1  (Op=‘J’)
=
=  (Op=‘lw’)
=  (Op=‘sw’)
=
=  (Op=‘J’)
 | NS3 | NS2 | NS1 | NS0
NextState0 | 0 | 0 | 0 | 0
NextState1 | 0 | 0 | 0 | 1
NextState2 | 0 | 0 | 1 | 0
NextState3 | 0 | 0 | 1 | 1
NextState4 | 0 | 1 | 0 | 0
NextState5 | 0 | 1 | 0 | 1
NextState6 | 0 | 1 | 1 | 0
NextState7 | 0 | 1 | 1 | 1
NextState8 | 1 | 0 | 0 | 0
NextState9 | 1 | 0 | 0 | 1
NS2
NS3
NS0
NS1

## Slide 19
NS1 = NextState2 + NextState3 + NextState6 + NextState7
NextState2 = …
NestState3 = …
NestState6 = …
NestState7 = …
 | NS3 | NS2 | NS1 | NS0
NextState0 | 0 | 0 | 0 | 0
NextState1 | 0 | 0 | 0 | 1
NextState2 | 0 | 0 | 1 | 0
NextState3 | 0 | 0 | 1 | 1
NextState4 | 0 | 1 | 0 | 0
NextState5 | 0 | 1 | 0 | 1
NextState6 | 0 | 1 | 1 | 0
NextState7 | 0 | 1 | 1 | 1
NextState8 | 1 | 0 | 0 | 0
NextState9 | 1 | 0 | 0 | 1

## Slide 20
 | NS3 | NS2 | NS1 | NS0
NextState0 | 0 | 0 | 0 | 0
NextState1 | 0 | 0 | 0 | 1
NextState2 | 0 | 0 | 1 | 0
NextState3 | 0 | 0 | 1 | 1
NextState4 | 0 | 1 | 0 | 0
NextState5 | 0 | 1 | 0 | 1
NextState6 | 0 | 1 | 1 | 0
NextState7 | 0 | 1 | 1 | 1
NextState8 | 1 | 0 | 0 | 0
NextState9 | 1 | 0 | 0 | 1

## Slide 21
21
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.5 The four truth tables for the four next-state output bits (NS[3–0]). The next-state outputs depend on the value of Op[5-0], which is the opcode field, and the current state, given by S[3–0]. The entries with X are don’t-care terms. Each entry with a don’t-care term corresponds to two entries, one with that input at 0 and one with that input at 1. Thus an entry with n don’t-care terms actually corresponds to 2n truth table entries.

## Slide 22
22
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.2 The control unit for MIPS will consist of some control logic and a register to hold the state. The state register is written at the active clock edge and is stable during the clock cycle
?

## Slide 24
24
Copyright © 2014 Elsevier Inc. All rights reserved.
Using Read-Only Memory (ROM)
Address
Content

## Slide 25
25
Copyright © 2014 Elsevier Inc. All rights reserved.
Using Read-Only Memory (ROM)
State
Control Signals

## Slide 26
26
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.2 The control unit for MIPS will consist of some control logic and a register to hold the state. The state register is written at the active clock edge and is stable during the clock cycle
ROM
S3
S2
S1
S0
ROM

## Slide 27
27
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.6 The truth table for the 16 datapath control outputs, which depend only on the state inputs. The values are determined from Figure D.3.4. Although there are 16 possible values for the 4-bit state field, only ten of these are used and are shown here. The ten possible values are shown at the top; each column shows the setting of the datapath control outputs for the state input value that appears at the top of the column. For example, when the state inputs are 0011 (state 3), the active datapath control outputs are IorD or MemRead.
16
Control signals
10 States

## Slide 28
28
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.7 The contents of the upper 16 bits of the ROM depend only on the state inputs. These values are the same as those in Figure D.3.6, simply rotated 90°. This set of control words would be duplicated 64 times for every possible value of the upper six bits of the address.
Address = State
Word = Control Signals

## Slide 29
29
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.8 This table contains the lower 4 bits of the control word (the NS outputs), which depend on both the state inputs, S[3–0], and the opcode, Op[5–0], which correspond to the instruction opcode. These values can be determined from Figure D.3.5. The opcode name is shown under the encoding in the heading. The four bits of the control word whose address is given by the current-state bits and Op bits are shown in each entry. For example, when the state input bits are 0000, the output is always 0001, independent of the other inputs; when the state is 2, the next state is don’t care for three of the inputs, 3 for lw, and 5 for sw. Together with the entries in Figure D.3.7, this table specifies the contents of the control unit ROM. For example, the word at address 1000110001 is obtained by finding the upper 16 bits in the table in Figure D.3.7 using only the state input bits (0001) and concatenating the lower four bits found by using the entire address (0001 to find the row and 100011 to find the column). The entry from Figure D.3.7 yields 0000000000011000, while the appropriate entry in the table immediately above is 0010. Thus the control word at address 1000110001 is 00000000000110000010. The column labeled “Any other value” applies only when the Op bits do not match one of the specified opcodes.
Next states

## Slide 30
State
f5 - f0
NextState
ROM
State
Control
ROM
…
…
16
210 = 1024 addresses
< 60 have contents
(only ~5% addresses used)
24 = 16 addresses
10 have contents

## Slide 31
31
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.4.1 The control unit using an explicit counter to compute the next state. In this control unit, the next state is computed using a counter (at least in some states). By comparison, Figure D.3.2 encodes the next state in the control logic for every state. In this control unit, the signals labeled AddrCtl control how the next state is determined.
NextState (0000-1001)
State (0000-1001)
Refined design
for NextState

## Slide 32
32
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.3.1 The finite-state diagram for multicycle control.

## Slide 33
33
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.4.2 This is the address select logic for the control unit of Figure D.4.1.
NextState (0000-1001)

## Slide 34
34
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.4.3 The dispatch ROMs each have 26 5 64 entries that are 4 bits wide, since that is the number of bits in the state encoding. This figure only shows the entries in the ROM that are of interest for this subset. The first column in each table indicates the value of Op, which is the address used to access the dispatch ROM. The second column shows the symbolic name of the opcode. The third column indicates the value at that address in the ROM.
When State1
When State2

## Slide 35
00: NextState = 0 – State4 + State5 + State7 + State8 + State9
01: NextState from ROM1 – State1 (depending on Op-code)
10: NextState from ROM2 – State2 (depending on Op-code)
11: NextState = State++ – State0 + State3 + State6
AddrCtl
State | AddrCtl
0000 | 11 (3)
0001 | 01 (1)
0010 | 10 (2)
0011 | 11 (3)
0100 | 00 (0)
0101 | 00 (0)
0110 | 11 (3)
0111 | 00 (0)
1000 | 00 (0)
1001 | 00 (0)
AddrCtl0 = State0 + State1
+ State3 + State6
= +
+ +
AddrCtl1 = ?

## Slide 36
36
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE D.4.4 The values of the address-control lines are set in the control word that corresponds to each state.