## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy

## Slide 2
2
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplified—the sign-extended immediate and branch logic are missing—this drawing gives the essence of the forwarding hardware requirements.

## Slide 3: Principle of Locality
Fact of programs:
During any period of time, a program accesses a relatively small proportion of its address space.
That is, related instructions/data tend to cluster together, instead of “jumping around”
This is true for both instruction space and data space
We wanted to take advantage of this fact, to make the computer run faster
§5.1 Introduction

## Slide 4: Principle of Locality
§5.1 Introduction
program
(instructions)
data (integers, arrays)

## Slide 5: Principle of Locality
Temporal locality
  Items (instructions or data) accessed recently are likely to be accessed again soon
  Examples:
    instructions in a loop
    recursive calls
§5.1 Introduction

## Slide 6: Principle of Locality
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  Examples:
    sequential instruction access
    array data
§5.1 Introduction

## Slide 7: Taking Advantage of Locality
The computer’s memory system is organized in hierarchy
Store everything on disk
  Hard drive (largest, cheap, permanent storage)
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory (smaller, more expensive)
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU (smallest, most expensive)

## Slide 8: Taking Advantage of Locality
The computer’s memory system is organized in hierarchy
Everything is eventually stored on disk
  Hard drive (largest, cheap, permanent storage)
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory (smaller, more expensive)
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU (smallest, most expensive)

## Slide 9: Taking Advantage of Locality
The computer’s memory system is organized in hierarchy
Everything is eventually stored on disk
  Hard drive (largest, cheap, permanent storage)
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory (smaller, more expensive)

## Slide 10: Taking Advantage of Locality
The computer’s memory system is organized in hierarchy
Everything is eventually stored on disk
  Hard drive (largest, cheap, permanent storage)
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory (smaller, more expensive, fast)
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU (smallest, most expensive, fastest)

## Slide 11: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Called Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent in upper
  Called Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
cache
RAM
Hit
Miss

## Slide 12: Memory Technology
Static RAM (SRAM, used by cache)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM) ≈ 100 times
  50ns – 70ns, $20 – $75 per GB
Magnetic disk ≈ 100 times
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory:
  Access time of cache
  Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 13: DRAM
Data (bits) are stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed (volatile)
    Refreshed by reading contents and writing back
    Performed on a DRAM “row”

## Slide 14: Raising DRAM Performance
Row buffer
  Allows several words to be read and refreshed in parallel (not just one word at a time)
Synchronous DRAM
  Consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Simultaneous access to multiple DRAM “banks”
  Improves bandwidth

## Slide 15: Increasing Memory Bandwidth
b. 4-word wide mem (15 cycles to connect to mem)
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  missed access (1), connect mem (15), load cache (1)
  Bandwidth = 16 bytes / 17 cycles = 0.94 bytes/cycle
c. 4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 bytes/cycle
Wider bus
Higher bandwidth
Memory banks

## Slide 16: Increasing Memory Bandwidth
b. 4-word wide mem (15 cycles to connect to mem)
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  missed access (1), connect mem (15), load cache (1)
  Bandwidth = 16 bytes / 17 cycles = 0.94 bytes/cycle
c. 4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 bytes/cycle
Wider bus
Higher bandwidth
Memory banks

## Slide 17: Increasing Memory Bandwidth
b. 4-word wide mem (15 cycles to connect to mem)
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  missed access (1), connect mem (15), load cache (1)
  Bandwidth = 16 bytes / 17 cycles = 0.94 bytes/cycle
c. 4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 bytes/cycle
Wider bus
Higher bandwidth
Memory banks

## Slide 18: Flash Storage (Solid State)
Nonvolatile semiconductor storage
  Faster than disk, but still slower than DRAM
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)
  SSD replacing magnetic drives
§6.4 Flash Storage

## Slide 19: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks

## Slide 20: Disk Storage (Hard Disk)
Nonvolatile, rotating magnetic storage
§6.3 Disk Storage

## Slide 21: Disk Storage (Hard Disk)
Nonvolatile, rotating magnetic storage
§6.3 Disk Storage

## Slide 22: Disk Sectors and Access
Each sector contains:
  Sector ID
  Data (512 bytes (0.5KB) - 4096 bytes (4KB))
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads (mechanical operation, slow)
  Rotational latency (mechanical operation, slow)
  Data transfer
  Controller overhead

## Slide 23: Disk Sectors and Access
Each sector contains:
  Sector ID
  Data (512 bytes (0.5KB) - 4096 bytes (4KB))
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves:
  Queuing delay if previous accesses are on-going
  Seek: turn the heads (mechanical operation, slow)
  Disk rotational latency (mechanical operation, slow)
  Data transfer
  Controller overhead

## Slide 24: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time (to read 1 sector (512B))
  4ms seek time (time of head turning) + ½ / (15,000/60) = 2ms avg rotational latency + 512B / 100MB/s ≈ 0.005ms transfer time + 0.2ms controller delay = 6.2ms (majority mechanical time)
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 25
25
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplified—the sign-extended immediate and branch logic are missing—this drawing gives the essence of the forwarding hardware requirements.

## Slide 26: Memory Hierarchy Levels
Cache Memory
Main Memory -- RAM

## Slide 27: Cache
Cache memory
  It is the level of the memory hierarchy closest to the CPU, the fastest, and the most costly
Given accesses X1, …, Xn–1, Xn (mem addr)
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?
Cache
Cache
Is xn in Cache?

## Slide 28: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  Cache address = (Block address) % (#Blocks in cache)
  In example below, 32-addr mem, 8-addr cache, 1-word block
If #Blocks is a power of 2, just use low-order address bits for Cache address
Cache
Mem
address in memory

## Slide 29: Tags and Valid Bits
Mem addresses
00001, 01001, 10001, 11001
will all be mapped to cache address 001
How do we know which particular word is currently in a cache location?
  Store the whole address along with the data
  Actually, only need to store the high-order bits (called “tag”)
What if there is no data in a cache address?
  Valid bit: 1 = present, 0 = not present; Initially 0

## Slide 30: Cache Example
8-blocks, 1 word/block, direct mapped
Address sequence: 22, 26, 22, 26, 16, 13, 16, 18
Initial cache state
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 0 |  | 
111 | 0 |  | 

## Slide 31: Cache Example
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 32: Cache Example
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 33: Cache Example
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 34: Cache Example
Index | V | Tag | Data
000 | 1 | 10 | Mem[10000]
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 1 | 00 | Mem[00011]
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 35: Cache Example
Index | V | Tag | Data
000 | 1 | 10 | Mem[10000]
001 | 0 |  | 
010 | 1 | 10 | Mem[10010]
011 | 1 | 00 | Mem[00011]
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 36: Address Subdivision

## Slide 37: Address Subdivision

## Slide 38: Larger Block Size - Example
64-block cache, 16 bytes/block (4-word)
  To what block number does byte address 1200 map?
Block address = 1200/16 = 75
Block number = 75 % 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
Block number

## Slide 39: Single-word vs. Multi-word Cache
single-word cache block
multi-word cache block

## Slide 40: Single-word vs. Multi-word Cache
single-word cache block

## Slide 41: Single-word vs. Multi-word Cache
(16 words)
(256
blocks)
16-word cache block

## Slide 42: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
  But it’s not always “the larger, the better”

## Slide 43: Block Size Considerations
In a fixed-sized cache
  Larger blocks  fewer blocks
    More competition  increased “block miss rate”
  Larger miss penalty
    When replacing a block due to miss, some soon-needed addrs may be swapped out
    Can cancel benefit of reduced miss rate
Need to determine an appropriate block size – tradeoff

## Slide 44: Block Size Considerations

## Slide 45: Memory Hierarchy Levels
Cache Memory
Main Memory -- RAM

## Slide 46: Cache Hits
Ex. lw $1, 0($2)
On cache hit, CPU proceeds normally
cache
RAM
Hit
lw $1, 0($2)

## Slide 47: Cache Misses
On cache miss
  Stall the CPU pipeline
  Fetch block from mem (lower level of hierarchy)
  After fetch:
  For instruction cache miss
    Restart instruction fetch
  For data cache miss
    Complete data access
cache
Hit
Miss
lw $1, 0($2)

## Slide 48: Write-Through (Issues on Hit)
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
5
5

## Slide 49: Write-Through (on Hit)
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
6
5
write

## Slide 50: Write-Through (on Hit)
Write-through: also update memory
6
6
write

## Slide 51: Write-Through (on Hit)
But that makes write operation take longer
  e.g., if base CPI = 1, 10% of instructions are stores (sw)
  Assume write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
  Due to write-through, “sw” instruction is a potentially more expensive instruction than “lw”

## Slide 52: Write-Through
Try to make it quicker: Use a “write buffer”
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full
  Put it aside first (buffering), and write later in a batch
write
buffer
6
6
5

## Slide 53: Alternative: Write-Back
On data-write hit, only update the block in cache (don’t write to mem)
  But keep track of whether each block is “dirty”
  “dirty” “has been written to”
When a dirty block is replaced
  Write it back to memory
  Can use a write-buffer to allow replacing block to be read first

## Slide 54: Write Allocation
What should happen on a write miss?
For write-through, two alternatives:
  1. Allocate on miss: fetch the block, then write
  2. Write-around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
    Don’t fetch the block until the first read-miss
For write-back
  Need to read into write-buffer in cache
  So need to fetch the block, and flag dirty

## Slide 55: Real example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline (we discussed 5-stage procsr)
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  I: Instruction; D: Data
  Each 16KB Cache: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates (real statistics)
  I-cache: 0.4% 99.6% of instructions fetched from cache
  D-cache: 11.4% 88.6% of data lw/sw in cache
  Weighted average miss rate: 3.2%

## Slide 56: Example: Intrinsity FastMATH

## Slide 57: Main Memory Supporting Caches
Use DRAMs for main memory
  Fixed width (e.g., 1 word)
  Connected by fixed-width clocked bus
    Bus clock is typically slower than CPU clock
Example cache block read (mem → cache)
  1 bus cycle for address transfer
  15 bus cycles per DRAM access
  1 bus cycle per data transfer

## Slide 58: Main Memory Supporting Caches
b. 4-word wide mem (15 cycles to connect to mem)
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  missed access (1), connect mem (15), load cache (1)
  Bandwidth = 16 bytes / 17 cycles = 0.94 bytes/cycle
c. 4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 bytes/cycle
Wider bus
Higher bandwidth
Memory banks
Memory
For 4-word block cache, 1-word-wide DRAM
  Miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  Bandwidth = 16 bytes / 65 cycles = 0.25 bytes/cycle

## Slide 59: Cache Performance Example
Given
  I-cache miss rate = 2% (instruction fetch)
  D-cache miss rate = 4% (data lw/sw)
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss penalty per instruction
  I-cache: 100% × 2% × 100 = 2
  D-cache: 36% × 4% × 100 = 1.44
Actual average CPI = 2 + 2 + 1.44 = 5.44
  5.44/2 =2.72 times slower than ideal CPU
1 cycle address transfer
1 data transfer
access cache
100% of times
36% of times need
to access again

## Slide 60: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 5%×20 = 2ns
    2 cycles per instruction
    (cache cycle, not memory cycle)

## Slide 61
61
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplified—the sign-extended immediate and branch logic are missing—this drawing gives the essence of the forwarding hardware requirements.

## Slide 62: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  Cache address = (Block address) % (#Blocks in cache)
  In example below, 32-addr mem, 8-addr cache, 1-word block
If #Blocks is a power of 2, just use low-order address bits for Cache address
Cache
Mem
address in memory

## Slide 63: Associative Caches
Purpose: To increase hit-rate
Fully associative
  Non-fixed mapping
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator (tags) at every entry (expensive)
Not fully associative: n-way set associative
  Cache is divided into several sets
  Allow a given block to go in any cache entry in a certain set

## Slide 64: Associative Caches

## Slide 65: Associative Caches
n-way set associative
  Each set contains n entries
  Block number (memory address) determines which set it can go
    Set # = (Block number) % (# of sets in cache)
  Search all entries in a given set at once
  n tag comparators (less expensive)

## Slide 66: Associative Cache Example
address 12 = 1100
address 12 = 1100
address 12 = 1100
Set # 0
Set # = 12 % 4 = 0
Set # = 12 % 1 = 0

## Slide 67: Spectrum of Associativity
For a cache with 8 entries
address 14 = 1110
address 14 = 1110
address 14 = 1110
address 14 = 1110
Set
0
(4 sets)
(2 sets)
(1 set)

## Slide 68: Associative Cache Example
Compare 4-block caches (00,01,10,11)
  Direct mapped (4 sets); 2-way associative (2 sets); fully associative (4-way, 1 set)
Consider block access sequence:
0, 8, 0, 6, 8

## Slide 69: Associative Cache Example
Block access sequence: 0, 8, 0, 6, 8
  i.e. 0000, 1000, 0000, 0110, 1000 (mem addr)
Direct mapped (4 sets)
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0:address ending 00 | 1:address ending 01 | 2:address ending 10 | 3:address ending 11
0 | 00 | miss | Mem[0] |  |  | 
8 | 00 | miss | Mem[8] |  |  | 
0 | 00 | miss | Mem[0] |  |  | 
6 | 10 | miss | Mem[0] |  | Mem[6] | 
8 | 00 | miss | Mem[8] |  | Mem[6] | 
time

## Slide 70: Associative Cache Example
2-way set associative (2 sets)
0000, 1000, 0000, 0110, 1000
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | set #0: Address ending with 0 |  | set #1: Address ending with 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative (1 set)
Block address |  | Hit/miss | Cache content after access Any address, one set of 4-words |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 71: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing gains
Simulation of a system with 64KB Data-cache, 16-word blocks, SPEC2000
  1-way: 10.3% (direct map)
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 72: Set Associative Cache Organization
4-way set associative
Mem[Tag(22bits) + 11111100]
Set # 11111100 (=252)
256 sets
4-word in each set

## Slide 73: Issue: Replacement Policy
2-way set associative
When Mem[0110] is loaded, replace Mem[8]
Block address | Cache index (set #) | Hit/miss | Cache content after access |  |  | 
 |  |  | Address ending with 0 (set #0) |  | Address ending with 1 (set #1) | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 

## Slide 74: Issue: Replacement Policy
2-way set associative
When Mem[0110] is loaded, replace Mem[0]
Issue: When Mem[0110] is loaded into cache, which word is to be replaced?
Block address | Cache index (set #) | Hit/miss | Cache content after access |  |  | 
 |  |  | Address ending with 0 (set #0) |  | Address ending with 1 (set #1) | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[6] | Mem[8] |  | 
8 | 0 | hit | Mem[6] | Mem[8] |  | 

## Slide 75: Issue: Replacement Policy
Direct mapped: no choice
Set associative
  Non-valid (not in use) entry first, if there is one
  Otherwise, choose among entries in the set
Least-Recently Used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way
    manageable for 4-way, but too hard beyond that (hard to keep track just by hardware)
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 77: Multi-level Caches
Primary cache attached to CPU
  Smallest, fastest, most expensive
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 78
Multi-level Caches
Level-2
Primary (L-1)

## Slide 79: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  (i.e. 4 × 109 cycles/sec = 0.25ns/per cycle)
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective (average) CPI
  = 1 + 2% × 400 = 1 + 8 = 9

## Slide 80: Example (cont.)
Now add L-2 cache
  Access time = 5ns (btwn L1-L2)
  Global miss rate to main memory = 0.5%
Primary miss, but L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles (btwn L1-L2)
Primary miss, and L-2 miss (global miss)
  Extra penalty = 400 cycles (btwn L2-main)
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 81: Multilevel Cache Considerations
Primary cache (L-1) design target
  Focus on small hit time (time to process hits, more hits expected)
L-2 cache design target
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results – since the smaller, the quicker
  L-1 cache smaller than a single-level cache
  L-1 block size smaller than L-2 block size

## Slide 82: Interactions with Advanced CPUs
Advanced CPUs can execute out-of-order instructions during cache-miss
  Pending (missed) sw stays in load/store unit
  Instructions dependent on missed instruction wait in reservation stations
  Instructions independent of the missed instruction can just continue
Effect of cache-miss depends on program data flow. Hard to analyze (because there’s no information in the code)

## Slide 83: Interactions with Software
Misses can also depend on memory access patterns
Determined by
  Algorithm behavior
  Compiler optimization for memory access

## Slide 84: Errors in Memory/Storage
Errors can happen during data transfer
  Bit 1 → 0
  Bit 0 → 1
Happen rarely, but still happen
So error detection is part of memory hierarchy system

## Slide 85
Recall that in hard disk:
Each sector contains:
  Sector ID
  Data (512 bytes (0.5KB) - 4096 bytes (4KB))
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Errors in Memory/Storage

## Slide 86: Error Detection - The Hamming SEC Code (Single-Error Correcting)
Hamming distance
  Number of bits that are different between two bit-patterns
Example: Hamming distance between 01101010 and
11011011 = 4

## Slide 87: Error Detection - The Hamming SEC Code
If the minimum (Hamming) distance between any two valid data is 2 – then we can detect single-bit errors
  E.g. parity code
  E.g. even parity: add a parity bit to data so that there’s always even number of 1s
If minimum distance = 3: provides single error correction, 2 bit error detection

## Slide 88: Even-Parity Code – Detect 1-Bit Error
We can know 1 bit was wrong (detect), but don’t know which bit (identify)
Ex. 00011→ 00111
00101→ 00111

## Slide 89: Encoding SEC – Identify 1-Bit Error
Now we want to do better
Would like to not only know bits are wrong, but also know which bit(s) are wrong
SEC – Single Error Correction

## Slide 90: Encoding SEC – Identify 1-Bit Error
To calculate Hamming SEC code:
  8 bits of real data; 4 more bits added for error detecting/locating -- 12 bits in total
  Number bits from 1 on the left
  All bit positions that are a power 2 are parity bits
  Each parity bit checks certain data bits. E.g.
    P1 is the parity bit for bits 1, 3, 5, 7, 9, 11
    P2 is the parity bit for bits 2, 3, 6, 7, 10, 11, etc.

## Slide 91: Encoding SEC Example
Even parity
Original data: __0_000_0000 (= 00000000)
Encoded data: 000000000000
Original data: __0_000_0001 (= 00000001)
Encoded data: 000100010001

## Slide 92: Encoding SEC Example
Original data: __0_000_0001 (= 00000001)
Encoded data: 000100010001
Received data: 000100010101
How do I know if there’s an error or not?
Error
Transfer / copy

## Slide 93: Decoding SEC
When receiving coded data, generate parity bits the same way
Value of parity bits indicates which bits are in error
  Use numbering from encoding procedure
  E.g. (0=even parity; 1=odd parity)
    Parity bits = 0000 indicates no error
    Non-zero parity bits mean there’s an error
    E.g. Parity bits = 0101 (read from right to left) indicates bit 10dec was flipped

## Slide 94: Encoding SEC Example
Original data: 00000000; even parity
Encoded data: 000000000000
Suppose bit-ten flipped: 000000000100
Received data parity bits: 0101 (bit-ten wrong)

## Slide 95: Encoding SEC Example
Original data: 00000001; even parity
Encoded data: 000100010001
Suppose bit-seven flipped: 000100110001
Received data parity bits: 1110 (bit 7 wrong)

## Slide 96: SEC/DED Code
Add one more parity bit (pn) for the whole word (data-bits + parity-bits)
Then we can correct (identify) 1-bit error, and detect 2-bit error
Decoding example: 4-bit data + 3-bit parity (H)
  Let H = SEC parity bits (3 bits)
    H even, pn even (0), no error (H 3 bits, pn 1 bit)
    H odd, pn odd (1), correctable single-bit error
    H even, pn odd (1), error in pn bit
    H odd, pn even (0), double error occurred (don’t know which 2)
ECC (Error Correcting Codes) DRAM uses SEC/DED with 8 bits protecting each 64 bits

## Slide 97: Virtual Memory
§5.7 Virtual Memory
Structure similar to memory-cache exists between disk and main memory
View main memory as a “cache” for disk (secondary) storage
Managed jointly by hardware and software (OS, operating system)
(memory-cache totally by hardware)

## Slide 98: Virtual Memory
§5.7 Virtual Memory

## Slide 99: Virtual Memory
Multiple programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a “page”
  VM translation “miss” is called a “page fault”
§5.7 Virtual Memory

## Slide 100: Address Translation
Page size is fixed (e.g., 4KB = 4096 Bytes)
Page Table
Mem (8~16G)
Disk (500G~1T)

## Slide 101: Page Fault Penalty
On page fault, the page must be fetched from disk to main memory
  Takes millions of clock cycles
  Handled by OS code (program, not hardware)
We certainly want to minimize page fault rate
  Placement policy – always fully associative
  That is, a page on disk can go to anywhere in memory
  Smart replacement algorithms

## Slide 102: Page Table
Placement information is stored in Page Table
  Array of page table entries, indexed by virtual page number (the whole disk)
  CPU has a Page Table Register, which points to the beginning of Page Table in physical memory

## Slide 103: Memory Hierarchy Levels
RAM (Memory)
Disk
Cache
4
103
17
102
101

## Slide 104: Page Tables
Page Table
(part of OS,
also in RAM)
(RAM)
17
102
4
103
17
4
101

## Slide 105: Page Tables
If page is present in memory
  PTE (Page Table Entry) stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 106: Translation Using a Page Table
220

## Slide 107: Mapping Pages to Storage
103
4
102
1
101

## Slide 108: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page (meaning it was just used)
  Periodically cleared to 0 by OS
  Meaning this page has not been used for a while
  So all “0” pages are candidates for replacement

## Slide 109: Replacement and Writes
Disk writes take millions of cycles
  Write a block (a page) at a time, not individual locations
  Write through (i.e. immediate write to disk) is impractical; not an option
  Use write-back
    That is, write to disk when page is being replaced
  “Dirty bit” in PTE is set every time the page is written

## Slide 110: Fast Translation Using a TLB
The Page Tables itself is in main memory
Address translation would require extra memory references
  First reference to access the Page Table Entry (PTE)
  Second reference is the actual memory access

## Slide 111: Fast Translation Using a TLB
However, access to page tables has good locality, which can be taken advantage of
  So use a fast cache of PTEs within the CPU
  Called Translation Look-aside Buffer (TLB)
  Typical TLB: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 112: Mapping Pages to Storage

## Slide 113: Fast Translation Using a TLB

## Slide 114: TLB Misses – Page not in TLB
Case 1: If page is in memory
  Load the PTE from memory to TLB and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler

## Slide 115: TLB Misses – Page not in TLB
Case 2: If page is not in memory - page fault
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 116: TLB Miss Handler
TLB miss indicates whether
  Page present (i.e. in RAM), but PTE not in TLB
  Or page not present (i.e. not in RAM)
Must recognize TLB miss before destination register overwritten
  Raise exception ( ex. lw $2, 0($1) )
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not in memory, page fault will occur

## Slide 117: Page Fault Handler
Fault -- Virtual address to PTE, find “not present” in memory (RAM)
Locate page on disk
Choose memory page to replace
  If the mem page is dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction

## Slide 118: TLB and Cache Interaction
If cache tag uses physical address
  Note that this example assumes virtual and physical pages have the same number of address bits (20 bits)
  However, physical addresses should be smaller numbers
  Cache
Cache

## Slide 119: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notion of caching
Issues at each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
§5.8 A Common Framework for Memory Hierarchies
The BIG Picture

## Slide 120: Mapping Pages to Storage
Cache
Magnetic disk/
Solid-state drive (SSD)
(512G~1TB)
(8~16GB)
(~8MB)

## Slide 121: Mapping Pages to Storage

## Slide 122: TLB and Cache Interaction
If cache tag uses physical address
  Note that this example assumes virtual and physical pages have the same number of address bits (20 bits)
  However, physical addresses should be smaller numbers
  Cache
Cache

## Slide 123: Block Placement
We want to load a page from disk storage to physical memory (RAM)
Issue: How to choose the location in physical memory?
For virtual memory, only full associativity is feasible

## Slide 124: Recall: Cache Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement, fast operation
  n-way set associative
    n choices within a set - limited flexibility
  Fully associative
    Any location - full flexibility
Higher associativity reduces miss rate
  But increases complexity/cost/access time

## Slide 125: Finding a Block
Caches (hardware, between RAM and cache)
  Reduce comparisons to reduce cost
Virtual memory (software, between disk and RAM)
  Full table lookup makes full associativity feasible
  Benefit: reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 126: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support
    Use-bit set to 1 on access to page (meaning this page was just accessed)
    Periodically cleared to 0
    Choose “0”-pages for replacement

## Slide 127: Write Policy
Write-through (cache only)
  Update both upper and lower levels
  Simplifies replacement; may require write buffer
Write-back (cache and virtual memory)
  Update upper level only
  Update lower level when block is replaced
  Need to keep more states
Virtual memory (disk-RAM)
  Only write-back is feasible, because disk-write latency is too long (millions of cycles)

## Slide 128: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block (unavoidable)
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache, multiple blocks have the same cache address
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 129: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block (unavoidable)
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache, multiple blocks have the same cache address
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 130: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block (unavoidable)
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache, multiple blocks have the same cache address
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 131: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to loading in unused data (cache pollution)

## Slide 132: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate (aka fetch on write)
  Block size: 4 words (16 bytes = 16 B)
  Cache size: 16 KB (1K blocks = 210 = 1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
§5.9 Using a Finite State Machine to Control A Simple Cache
tag
index
offset
0
3
4
13
14
31
4 bits
10 bits
18 bits

## Slide 133: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access
4-word block
= 128 bits

## Slide 134: Finite State Machines for a Cache Controller
Use an FSM to sequence control steps
Set of states, transition on each clock edge
  State values are binary encoded
  Current state stored in a register
  Next state = fn (current state, current inputs)
Control output signals = fo (current state)

## Slide 135: Cache Controller FSM

## Slide 136: Cache Controller FSM
Could partition into separate states to reduce clock cycle time
No memory
access

## Slide 137: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to Mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
CPU
A
X: 0
CPU
B
X: 0
Cache A
X: 0
RAM (Mem)
Cache B

## Slide 138: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to Mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
CPU
A
X: 1
CPU
B
X: 0
X: 0
A Write “1” to X
Cache A
RAM (Mem)
Cache B

## Slide 139: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to Mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
CPU
A
X: 1
CPU
B
X: 0
X: 1
Write-through
A Write “1” to X
Cache A
RAM (Mem)
Cache B

## Slide 140: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to Mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
CPU
A
X: 1
CPU
B
X: 0
X: 1
Write-through
B Reads X Wrong!
A Write “1” to X
Cache A
RAM (Mem)
Cache B

## Slide 141: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to Mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
CPU
A
X: 1
CPU
B
X: 0
X: 1
Write-through
B Reads X Wrong!
A Write “1” to X
Coherence Problem!
Cache A
RAM (Mem)
Cache B

## Slide 142: Cache Coherence Problem
For multi-core, shared-memory processors
Suppose two CPU cores share a physical address space
  Write-through caches (write to mem immediately)
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | X: 0
1 | CPU A reads addr. X | 0 |  | X: 0
2 | CPU B reads X | 0 | 0 | X: 0
3 | CPU A writes 1 to X | 1 | 0 | X: 1

## Slide 143: Define What “Coherence” Means
Informally: Reads should always return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later, after X in P2’s cache is updated)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, then P2 writes X  all processors see writes in the same order
    End up with the same final value for mem addr X

## Slide 144: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache will be a miss
    Owning cache supplies updated value
CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
 |  |  |  | 0
CPU A reads X | Cache miss for X | 0 |  | 0
CPU B reads X | Cache miss for X | 0 | 0 | 0
CPU A writes 1 to X | Invalidate for X | 1 | Invalid | 1
CPU B reads X | Cache miss for X | 1 | 1 | 1

## Slide 145: Memory Consistency
Make sure writes seen by other processors
  “Seen” means a read returns the written value
  Can’t be instantaneously – should read “sufficiently” later after write
Assumptions
  A write completes only when all processors have seen it – wait sufficiently long after actual write
  A processor does not reorder writes with other accesses
Consequence
  P writes X then writes Y  all processors that see new Y also see new X
  Processors can reorder reads, but not writes

## Slide 146: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors
§5.16 Concluding Remarks